## Slide 1: 5G WIRELESS NETWORKS
Dr. Cenk M. Yetis and Assoc. Prof. Pontus Giselsson
Automatic Control Department
Lund University
https://tinyurl.com/inspirationalcoffee
Inspirational Coffee
November 13th, 2020
Notes: Today, I will talk about 2 elements in 5G networks, beam selection and channel estimation
Beam selection is also about channel estimation, we will see that in the next slides
This is the second version of the slides. I uploaded this version on Dropbox as well
In this version, I tailored the talk even more for the Control department to cover the fundamental concepts
I hope you will find the slides interesting
So, I cannot cover all the slides today
So, for those who are interested further, you can check this link on Monday. There, you will find a video of me going through the slides that I have not covered today
Today, we might have guest students (of Prof. Bernhardsson) from the electronics department

## Slide 2: CONTENTS
5G Wireless networks…………………………………………………………………… 1
Contents …………………………………………………………………………………… 2
PART – I – Overviews
MIMO channel …………………………………………………………………………… 5
Training phase ………………….. ……………………………………………………… 6
Beam training …… ……………………..……………………………………………… 8
mmWave overview ……………………..…………………………………………….. 9
5G conspiracies … … ……………………..…………………………………………… 16
Notes: The talk is composed of 3 parts
Part I is the basics, which will take up most of the time in this talk

## Slide 3: CONTENTS
PART - II
WASP-Beam training …………..……………………………………………………… 17
Cellular network vs. cell-free network …………..……………………………… 18
Challenges ………………………………………………………………………………… 19
Multi-Label problems………………………………………………………………….. 20
Numerical results ……………………………………………………………………….. 23
Notes: Part II is about our beam selection paper which I will go through briefly

## Slide 4: CONTENTS
PART - III
WASP-Channel estimation…………………………………………………………….. 25
Channel training …………………………….…………………………………………. 27
Acquisition of channel state information …………………………………………. 29
Compressed sensing based … ………………………………………………………… 30
Sparse channel estimation …………………………………………………………….. 31
Compressed sensing … … … ………………………………………………………… .. 34
Channel training … …………………………………………………………………….. 40
Compressed sensing recovery ……………………………………………………….. 41
Orthogonal matching pursuit (OMP) ………………………………………………… 45
Iterative thresholding algorithms ………………………………………………….. 46
Iterative thresholding algorithms – ISTA ………………………………………….. 47
Iterative thresholding algorithms – AMP …………………………………………… 50
Approximate message passing (AMP) ……………………………………………….. 52
Denoising based algorithms ……………………………………………………………..53
Bayesian inference models ……………………………………………………………...54
Application of AMP to Bayesian Inference Framework …………………………..56
Numerical results …………………………………………………………………………..58
References …………………………………………………………………………………….59
Notes: Part III is about channel estimation. I will not have time to go through this section unfortunately
As I said, you can check the link on Monday
As a future note, I plan to prepare one more talk about only the message passing algorithms. So, I will record again or let you know the Zoom link when the talk is available. I will email about this to the department

## Slide 5
. Different statistical properties based on the technology
(Transmitted symbols)
(Transmit beamforming matrix)
: Transmit beamforming vector for the stream i
to be transmitted from N antennas
Multiple-Input Multiple-Output (MIMO)
Channel
MIMO CHANNEL
Transmitted symbols:
Notes: This slide is from the last year’s presentation as a recap. This is the equation that we are interested in
y is the received signal vector …
There is a random complex number between each pair of antennas. We stack these numbers in a matrix called channel matrix
The transmitted signal x is U times s. s is the vector of transmitted symbols which we eventually want to decode (or in other words estimate) at the receiver. These symbols can be like 1s and 0s as in computer systems, or 1+, 1-js if we use QPSK constellation
The U matrix is called beamforming matrix. Each of its column affects a symbol, the 1st column affects the 1st symbol, the 2nd…, and so on.
By designing the U matrix, you form a beam to transmit a symbol on the beam, you can say so. Sometimes the word stream is used instead of symbol because we keep sending/streaming the symbols
The U matrix must be designed during the training phase which is right before the data transmission phase

## Slide 6
where (data transmission)
Training phase exists before the data transmission phase
must be designed during the training phase
  Design based on (a function of ). In general, this is called channel state information at the transmitter (CSIT)
  e.g., Channel estimation (channel training):
  Step 1) Estimate the channel matrix
  Step 2) Design based on (imperfect CSIT)
  Design based on (a function of something else). No CSIT
  e.g., Beam selection (beam training) (a greedy approach):
  Step 1) Create a set of beamforming options, where is
  the number of beamforming options
  Step 2) Select the columns (beamforming vectors) of from the set
TRAINING PHASE
Notes: So, we must have a training phase before the data transmission phase
must be designed during the training phase
The U matrix can be designed based on a function of the channel matrix. In general, …
Or, the U matrix can be designed based on something else, not based on the channel. This is called no CSIT in general
For the first option, for instance, you can do channel estimation
Then you optimize the U matrix based on the estimated channel values, which can be called imperfect CSIT
Sometimes, you can assume you know the exact H, which is called perfect CSIT, which is not a realistic assumption of course
For the second option, for instance, you can do beam selection. Here, a beamforming vector is shortly called as a beam
It can be also called beam training. As you know, selection algorithms are usually called greedy approaches
In this approach, first, you create a set of beamforming options based on some reasoning
Then you select each of your beamforming vectors (beams) out of this set
In this option, clearly, you are avoiding to do a channel estimation
So, we must have a training phase before the data transmission phase
𝐔 must be designed during the training phase
The U matrix can be designed based on a function of the channel matrix. In general, …
Or, the U matrix can be designed based on something else, not based on the channel. This is called no CSIT in general
For the first option, for instance, you can do channel estimation
Then you optimize the U matrix based on the estimated channel values, which can be called imperfect CSIT
Sometimes, you can assume you know the exact H, which is called perfect CSIT, which is not a realistic assumption of course
For the second option, for instance, you can do beam selection. Here, a beamforming vector is shortly called as a beam
It can be also called beam training. As you know, selection algorithms are usually called greedy approaches
In this approach, first, you create a set of beamforming options based on something
Then you select each of your beamforming vectors (beams) out of this set
In this option, clearly, you are avoiding to do a channel estimation

## Slide 7: TRAINING PHASE
Before the data transmission phase, the training phase is needed
During the training and data transmission phases, the assumption is that
  the channel matrix H stays constant
Training phase
  Channel training (channel estimation). Conventional approach
  Beam training (beam selection)
    Introduced and preferred for 5G mmWave communications where we have many antennas
    Channel estimation is avoided since it can be challenging with many antennas in terms of
      Computation
      Hardware
    A trivial linear beam selection algorithm is observed to provide satisfactory results with low complexity and simple hardware
Training phase
Training phase
Data transmission phase
…
Data transmission phase
Notes: To repeat, before the data transmission phase, we need a training phase to design the U matrix with or without CSIT
Here the assumption is that, during the …, does not change
  For both training options, either you do channel or beam training, the training and data transmission phases must be cyclic
  That is, each time the channel changes, you need to do a training before the data transmission phase
So, again, for the training phase, we can prefer the channel training option which is a conventional approach
Or, we can choose the beam training approach which is introduced and preferred for 5G networks where we have many antennas
Here, channel estimation is avoided because channel estimation can be challenging with many antennas in terms of
computational complexity and hardware
In fact, a proper beam selection can also be computationally complex and costly in hardware since the B number, the number of beam options to select from can become a large number easily
However, a simple and trivial linear beam selection algorithm is observed to …
So, currently, beam selection is selected in the 5G standards

## Slide 8: BEAM TRAINING
Assume we have predefined beams
Selection Metric Option-1
Direct link power
and so on…
Continue with access point (AP) 3 for user 1
Redo with all APs for user 2
Beam selection (linear)
Notes: Let’s have a look at the linear beam approach, which is very straightforward
Here is a case where we have 3 transmitters, and 2 receivers.
We assume we have only two beam options to select from for simplicity
First, we can start with receiver-1 (sometimes it is called user-1)
While all other APs are silent, AP-1 tests each of the beams to see which beam achieves the best performance
  Here, your performance metric is the received signal power, which can be called the direct link power
  Basically, you select the beam which is more directed towards the user
Then while all other APs are silent, this time AP-2 tests the beam options …
Each AP selects a beam for user-1, the algorithm continues with user-2
This is the trivial algorithm accepted in 5G standards

## Slide 9: mmWave OVERVIEW
Wavelength formula:
(spatial period)
: Wavelength (m)
: Frequency (Hz)
: Speed of light (m/s)
E.g.,
For a signal with GHz
For a signal with GHz
©
4G: microwave signals
5G: microwave signals + mmWave signals
Notes: In 5G, we will have mmWave signals in addition to microwave signals that we currently have in 4G
What is a microwave or mmWave signal?
The wavelength of your wave (signal) is given as, lambda=… It is a period in spatial domain (space domain) in meters
Like the periods of sinusoidal waves we are used to see in the time domain. The only difference is this is in the space (spatial) domain because we have speed parameter here, c. If there is no c, this will be the time domain, and this will be the period of the signal in seconds
For 3/4G microwave frequencies, you can talk about 800 MHz, 1.8 GHz, and 2.1 GHz frequencies for instance
For 5G mmWave frequencies, you can talk about 30 GHz ranges
So when you look at the wavelengths of these signals, they are both in the order of 1 mm, not in the order of 1 micrometer
But for some reason, you can Google this, people ask the same question also, if the wavelength is larger than 10 mm it is called microwave (Perhaps one reason is micro in Greek language might mean small, but I am not sure)
And if the wavelength is between 10 mm and 1 mm, it is called mmWave

## Slide 10: mmWave OVERVIEW
© Efficient Radar Forward Operator for Operational Data Assimilation within the COSMO-mode by Zeng
Notes: As seen in this figure, and as we know from the wavelength formula, as the frequency increases, the wavelength of the signal decreases
What does this mean?
You can say that the frequency is approximately equal to inverse of time t.
Then the wavelength equation is like a distance formula traveled by a car which is given by x=vt, as you know
Then the wavelength is the distance a signal can travel in a full cycle
Therefore, when the frequency is higher, the wavelength of your signal is smaller which means that your signal can travel less distance in space (or spatial domain)

## Slide 11: mmWave OVERVIEW
Some disadvantages
  The wave can travel less distance
  More transmit power at the transmitter is needed to travel the same distance
  More expensive and less stable equipment
Some advantages
  The spectrum is less crowded
  The bandwidth is wider
  More antennas can be packed
    Antenna length
    Distance between the two antennas
©
Radio stripes
©
Notes: So, this is a disadvantage, the signal can travel less distance
Or, to travel the same distance at a higher frequency, you need to send the signal from the transmitter with a higher power. So this is also a disadvantage
Also, equipment can be more costly and less stable at higher frequencies
So what is the advantage of higher frequencies then?
At higher frequencies, the spectrum is less crowded and the bandwidth ... I will talk about these two new terms in the next slide
Another advantage is that more antennas can be packed in the same area because the antenna length and the distance that must be between the two antennas are inversely proportional with f
Here you see a phone that can have 4 antennas at the edges
In fact, in future, it will be very different from today. Ericsson plans to have radio stripes. This is a long plastic like looking antenna which can be placed along the walls at a stadium, university etc.
The cellular BSs will be also different, I will show them later

## Slide 12: mmWave OVERVIEW
E.g., voice signal
Spectrum: The range of frequencies a signal has vs. the amplitude
Bandwidth: The difference between the maximum and minimum frequency values
©
Bandwidth
Center frequency
Notes: Let’s see the meanings of spectrum and bandwidth
Our voice is also a signal, so let’s explain these terms on a voice signal
Spectrum: …
Bandwidth: …The max-min frequency difference
So the spectrum is the whole figure whereas BW is only this distance
In a spectrum, you have the amplitude information per frequency, BW, and the center frequency of your signal

## Slide 13: mmWave OVERVIEW
At lower frequencies
  The spectrum is more crowded
  Bandwidths are narrower
Examples
  WLAN at 2.4 GHz and 5 GHz (center frequency)
  Bluetooth at 2.45 GHz (Microwave oven-noise)
  DECT phones at 1.9 GHz
© Viability of business models for multi-operator Wi-Fi coordination platforms by Dittrich and Hartog
Notes: At lower frequencies, the spectrum is congested. Therefore, you cannot have contiguous wide bandwidths at lower frequencies
As examples, WLANs operate at …
The handset and the main part of DECT phones talk to each other
The reason we have now 5 GHz as an additional option to 2.4 GHz for our WiFi routers at home is same because WiFi signals at 2.4 GHz are congested as you see in this figure
This figure shows the WiFi spots around some test location
You can get a similar plot by yourselves at your home with your PC and router after downloading a generic free software
If you live in a congested area, you might prefer 5 GHz because perhaps
  some people are still using old routers (now nearly impossible) that have only 2.4 GHz
  As I said, at high frequencies such 5 GHz, signals cannot travel (also cannot penetrate, e.g., the walls) much, so some people might want to insist to use 2.4 GHz
  Some people may not know anything about 5 GHz option
What if everyone chooses 5 GHz option?
  Then, the bandwidth effect comes in the picture. At higher center frequencies, you can have larger bandwidths as I explained
  Because it is like metropolitan area versus desert. Bandwidth is scarcer (more precious) at lower frequencies than higher frequencies. So at higher center frequencies, we can have larger bandwidths so that we can all share this wide bandwidth

## Slide 14: mmWave OVERVIEW
4/5G: 1, 2, 3, 4
Hybrid
©
4G
5G
5G
©
Notes: Here is a table for 4 and 5G networks
In 5G, we still use the same bands from 4G networks,
  There are some new additional bands
  The already existing bands are renamed with n and then the band number
So the first two tables are nearly same
But in the last table, we have the additional mmWave frequencies
It is called FR-1 (existing + few more bands), FR-2 mmWave frequencies
These are the band numbers, just n is added
The list is longer of course, I cut a part of it
This column indicates the center frequencies. Here it is MHz and here it is GHz
This column indicates the bandwidths. Both are MHz values but here you see values of 100, 200, and 400, whereas here, you see a maximum value of 50 Hz only
In short, in 5G, we use the existing microwave frequencies from 4G plus the new mmWave frequencies

## Slide 15: mmWave OVERVIEW
Power and penetration: 1
Very directional: 1 (Page 12, 15), 2 (last figure), 3, 4, 5, 6, 7, 8, 9, 10
©
20 km
500 m
Initial phase:
Indoor: Shopping malls, concert/seminar halls
Outdoor: Stadiums, downtown
Notes: Here you see speed… comparison of 4 and 5G networks
The speed is high as one of the reasons being said that we have large bandwidths in 5GLatency is also low in 5G networks for which I will give one of the reasons soon
The distance and penetration disadvantages are similar concepts
The range (distance) is low because the signal cannot travel far as I explained
Also, the smaller wavelength means the signal is more susceptible to even rain and fog
Penetrating through the walls is also more difficult
As a remedy to the disadvantages of mmWave signals, the 5G signals will be very directional in contrast to 4G
Assume these are all mmWave signals, if you can make your beam focused rather than wide, you can reach the receiver before your signal fades away (since mmWave signals cannot travel far)
As you see here, this focused signal can reach further
Focusing is achieved by using more antenna elements. (As I said earlier, we can pack more antennas in the same area at mmWave frequencies)
However, being focused brings another disadvantage. For instance, even the slightest movements of our heads become a problem at mmWave because the waves are very directional
So you can track the user by using all these four antennas. Or you can switch to the other beam if the user moves in this direction. Here, the two antennas generate two beams at two different frequencies (not to interference each other)
As you see here, the antennas will be in an array structure. The antenna can be an array of size 64x64, 128x128 etc.
Each of this small circle or rectangle is an antenna
These are the generations of base stations. At 5G, we move to this active antenna era. Here you see a BS with a single antenna, multiple antennas, more multiple antennas, then eventually BSs with many antenna elements in array structures. These both BSs can be called massive MIMO, it is up to you where you draw the line for the number of antennas to be called a massive MIMO system
So, in short, in 4G, waves are wider whereas in 5G, they are very directional
Since 5G signals cannot travel far, the mini-BSs will be everywhere, perhaps every 100, 500 meters, we will have mini-BSs
So this is one reason latency will be low in 5G networks
So in the initial phase, 5G will not be everywhere but in the shopping malls…
So, as a joke, if you plan to commit a criminal activity, you need to think twice this time because they will know your precise location almost : )
Whereas in 4G, they can know your whereabouts. If you are in downtown, it can be more precise, because there are more base stations in downtowns, but in 5G, it can be always precise

## Slide 16: 5G CONSPIRACIES
Health risks: 1, 2, 3a, 3b, 4
  The only documented health risk from mobile radiation is the heating of body tissues. Radiation safety limits are made to prevent this from happening
  For most users of 3G and 4G technology, it is easy to stay on the right side of these limits: They are only reached or exceeded if you are directly in front of a base station and less than 10 meters away
Notes: Thanks to this presentation, I just realized there are amazing conspiracies on 5G networks such as the famous virus can travel on 5G waves as noted on WHOs (world health organization’s) website saying that this is not true
I am not sure about 5G yet, but as you also know, it is good to stay away from 4G BSs
Probably it is the same in Sweden I guess, sometimes telecom operators offer some residential buildings a rental fee in return to put their BSs on top of the buildings. Although the price might be convincing, you really do not want to live on the last two floors of the building
It is the same idea with microwave ovens.
If you put your hand in it, it is no good
If you power it sometimes and try to stay away from it, it is good
But if you power it 24/7 and stay next to it, it is no good at all

## Slide 17: WASP – BEAM TRAINING
Team members:
Dr. Cenk M. Yetis - Lund University
Prof. Pontus Giselsson - Lund University
Prof. Emil Björnson - Linköping University (→| KTH)
Proposed a joint analog beam selection and digital beamforming design (1) in millimeter wave (2) cell-free (3) massive MIMO (4) systems
Components (1, 2, and 4) are expected in 5G networks. Cell-free component (3) is a candidate for 6G networks
The complexities of the proposed beam selection algorithms can still be overwhelming in practice
Proposed supervised machine learning (ML) algorithms that can be trained
off-line
62% Matlab, 38% Python with Scikit-Learn (Scikit-MultiLearn)
Notes: In this work, it was 3 of us.
We proposed a …
Components 1, 2, …
We proposed more advanced nonetheless still simple beam selection algorithms because the complexity can increase very quickly as I said
Even though we propose effective and simpler beam selection algorithms, the complexity can still be high when the network size grows, such as large number of APs, users, antennas, and large number of symbols we want to transmit per user
So we also propose ML algorithms which are trained off-line by our proposed beam selection algorithms

## Slide 18: CELLULAR NETWORK vs. CELL–FREE NETWORK
Cell-free networks consist of
many distributed access points (APs) with simple components
that jointly serve the users.
Notes: Unfortunately, I will skip these slides because there is no time

## Slide 19: CHALLENGES
BCC introduces patterns on the decision outputs in the beam selection problems
predefined beams

## Slide 20: MULTI-LABEL PROBLEMS
Assume .
4
, number of training samples
: features - direct link powers, : labels
Training Samples |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 0 | 5 | 3 | 0 | 5 | 
 |  |  |  |  |  |  |  | 1 | 6 | 0 | 3 | 2 | 
Training Samples |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 0 | 5 | 3 | 0 | 5 | 
 |  |  |  |  |  |  |  | 1 | 6 | 0 | 3 | 2 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 1 | 6 | 0 | 3 | 2 | 
Notation simplification:

## Slide 21: MULTI-LABEL PROBLEMS
Binary relevance: single label (i.e., multi-class problem) classification problems
Classifier chains: single label classification problems
 | 0
 | 1
 | 0
 | 1
 | 5
 | 6
 | 5
 | 6
 | 5
 | 6
 | 5
 | 6
 | 3
 | 0
 | 3
 | 0
 | 0
 | 3
 | 0
 | 3
 | 5
 | 2
 | 5
 | 2
 | 0
 | 1
 | 0
 | 1
 | 3
 | 0
 | 3
 | 0
 | 0
 | 3
 | 0
 | 3
 | 5
 | 2
 | 5
 | 2

## Slide 22: MULTI-LABEL PROBLEMS
Label Powerset:
 | 0 | 5 | 3 | 0 | 5 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 2 | 1 | 0 | 4 | 3 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 2 | 1 | 0 | 4 | 3 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 0
 | 0
 | 1
 | 2
 | 2
 | 0
 | 0
 | 1
 | 2
 | 2
 | 0 | 5 | 3 | 0 | 5 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 2 | 1 | 0 | 4 | 3 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 0 | 5 | 3 | 0 | 5 | 
 | 2 | 1 | 0 | 4 | 3 | 
 | 1 | 6 | 0 | 3 | 2 | 
 | 1 | 6 | 0 | 3 | 2 | 

## Slide 23: NUMERICAL RESULTS
Sum-rates and simulation durations of selection algorithms
init: Number of initializations
iter: Number of iterations
Chart: 
| Linear-DL-Disjoint | Linear-II-DL | Linear-II-Rate | Linear-IIS-Rate | Semi-linear-II-Rate
init=5, iter=3 | 0.0082767 | 0.015706 | 0.034437 | 0.058186
init=2, iter=2 | 0.0044404 | 0.0062348 | 0.011154 | 0.01862
init=1, iter=1 | 0.0033468 | 0.0037419 | 0.0042965 | 0.0055405 | 0.008456
Linear & Direct link power metric (DL)
(Disjoint design. All others are joint designs)
Linear & DL
Linear & Sum-rate metric*
Semi-centralized & Sum-rate
Linear & Sum-rate & Selection
*Sum-rate metric is not noted in the figure for brevity
network
Notes: Here you see the sum-rate results and corresponding simulation durations of some advanced beam searching algorithms for some network size
Sum-rates are in b/s/Hz
The lowest sum-rate and the lowest run time here and here belong to that trivial linear search algorithm
If you can consider this grey line only, you can say that you can either choose this or this algorithm
Because there is a substantial increase in the sum-rate with a little increase in the simulation duration for these two algorithms
However, after this point, sum-rate does not advance much while the simulation time starts steeping up
The other two more colourful results are for random number of initializations and iterations
Whereas for the grey plot, the number of initializations and iterations is 1 for each
For the beam searching algorithm, you need to make random beam initializations for all users before the algorithm starts
  Random initializations are not needed for the algorithms that use direct link metric but needed for the advanced algorithms
  By random initializations, you may find a better point to start with so that perhaps you end up at a better local optimum
The number of iterations equals to 2 for instance means that in the first iteration, you select beams for all APs, but you do one more iteration, and select beams for all APs one more time
The number of initializations and iterations are not helping much to increase the sum-rate because we assume single-antenna users here.
If we assume multiple antenna users, the selection complexity increases a lot suddenly, which may require GPUs rather than CPUs for the simulations. Therefore, in this work, we only investigated only single antenna user cases

## Slide 24: NUMERICAL RESULTS
Sum-rates of ML algorithms
network
Linear-II-Rate algorithm
with init=2 and iter=2 is used
for the training
Chart: 
| LSVM | GSVM | MLP | RF & DL | RF (init=1, iter=1) | RF | RF & Sel.
 | 8.1661 | 12.8514 | 19.3573 | 20.9669 | 21.6898 | 21.7699 | 21.8023
 | 21.947 | 21.947 | 21.947 | 21.947 | 21.947 | 21.947 | 21.947
RF & DL: Random forest & Direct link power metric
(All others use sum-rate metrics)
RF (init=1,iter=1): Only for this case
linear-II-Rate algorithm with init=1 and iter=1 is used
for the training
LSVM: Linear support vector machine
GSVM: Gaussian SVM
MLP: Multi-layer perceptron
Simulation durations:
RF-01:30, MLP-01:00, GSVM-15:00, and LSVM-00:05 (mm:ss)
Linear-II-Rate-12:00
Notes: Here we see the sum-rate results of machine learning algorithms
We use normal support vector machines, SVMs with Gaussian kernels, multi-layer perceptron, and random forests algorithms
RF gives the best results
This straight dashed line is the beam selection algorithm that is used to train these ML algorithms
As you see, RF algorithms can achieve sum-rates between 96-99% of the original results

## Slide 25: WASP – CHANNEL ESTIMATION
Team members:
Dr. Cenk M. Yetis - Lund University
Prof. Pontus Giselsson - Lund University
Dr. Özlem Tugfe Demir - Linköping University (|→ KTH)
Prof. Emil Björnson - Linköping University (→| KTH)
International Telecommunication Union (ITU) challenge in Artificial Intelligence (AI) and Machine Learning (ML) for 5G networks – ITU AI/ML in 5G Challenge
There are about 40 chapters
Off-line competition (few months)
International Collegiate Programming Contest (ICPC) challenge
  On-line competition (few hours)
Notes: This is the second part of the inspirational coffee hour at the Control Department of LU
In the first part, I mainly talked about mmWave channels and beam selection
In this second part, I will talk about channel estimation. In this work, it is 4 of us.
I and Prof. Pontus at LU and another postdoc Özlem and Prof. Emil at LU. They might be moving to KTH soon though
This year, we have noticed that there is a competition organized by a European union called ITU
The competition is about AI and ML in 5G networks
The competition has challenges about 40 topics in wireless networks. The topics range from coding and decoding of signals to beam selection, channel estimation, and so on
For each chapter, there is a common test data that has to be used by every team.
The competition is off-line; that is, they give you a few months to submit your results
I have also noticed that there is another competition, only for undergrad and grad students if I am not wrong
This competition is online. That is, teams with 5-6 members sit at a desk with computers, and other gadgets needed for the competition. Then they try to solve a given problem in a few hours

## Slide 26: WASP – CHANNEL ESTIMATION
Proposed a sparse channel estimation algorithm to be used for the training of ML algorithms
Proposed expectation maximization (EM) vector approximate message passing (VAMP) application to Bayesian inference framework [Rangan2019], i.e., statistical approaches, compressed sensing techniques
Deterministic approaches, e.g.,
Matlab object-oriented programming (AMP-Matlab) and TensorFlow (AMP-Deep Learning).
Continued to build on these existing libraries
Prof. Phil Schniter, Prof. Chao-Kai Wen
Sparse Bayesian learning proposed by the other post-doc won the 2nd place at the ITU competition (3rd place, Prof. Chandra Murthy)
Notes: In this work, we propose a sparse …
In this talk, I will focus on only the sparse channel estimation part, not the ML part
As I mentioned in the first part of the presentation, channel estimation has been the conventional approach in wireless networks. However, with the advent of mmWave signals in 5G networks, beam selection has become an esteemed option for 5G networks
In 5G, we cannot use conventional channel estimation techniques anymore. We need sparse channel estimation techniques rather than conventional non-sparse channel estimation techniques
I believe another reason why a trivial beam selection is accepted in 5G standards is that there is still more research needed on the sparse channel estimation techniques
Perhaps we will see a sparse channel estimation approach in the next release of 5G standards
In our work, we use an existing algorithm in the literature called EM …
This part will be discussed at the next presentation because as you see here, there are 4 different topics that need to be covered. EM, AMP, VAMP, and Bayesian inference
In this talk, I will give only an overview introduction to AMP
The next presentation might be ready in January or February. Again, I will upload the video and slides on the same link seen on the first page of the presentation
You can say that these are statistical approaches which are known as CS techniques
In this presentation, I will talk why we need to do sparse channel estimation and why we can use compressed sensing techniques to achieve this.
Then I will talk about the deterministic approaches such as minimization for sparse channel estimation
Finally, I will end the talk with brief connections between deterministic and statistical approaches
In our work, we use the existing libraries written in Matlab for the estimation part and TensorFlow for the ML part.
In general, we follow the footsteps of Prof. Schniter, who has publications and open-access libraries on these topics
The sparse Bayesian learning approach proposed by the …
The team who won the 3rd place also used SBL. They uploaded a short description of their proposal here
The results of 2nd and 3rd places came close. As far as I see, Özlem utilized some other features of mmWave channels as well, so she could have that winning margin
In fact, the methodology I use is also similar as you see here, it reads Bayesian inference
A reason I choose VAMP is that the messages are passed in vector forms. So that at every step, you do vector updates instead of scalar updates and I like to work with matrices and vectors.
Another reason is that VAMP is proposed by Prof. Schniter. I visited his lab for 6 months on a Turkish scholarship when I quit my full-time job to initiate my PhD thesis research right after completing my PhD courses
To attend the lectures at the university, I compensated the missing work hours by working over-time at a Turkish telecom company, which has always been in top-3 mobile service providers in Turkey
I am interested in Prof. Wen’s works as well. I met him in Taiwan. Thanks to this competition, I noticed Prof. Wen has also been doing research on these topics
Prof. Wen replied my Asst. Prof. application positive when I was in Taiwan. However, I really liked the scope of the WASP project here and the Profs I will be working with. So I chose this position instead
In this work, we propose a sparse …
In this talk, I will focus on only the sparse channel estimation part, not the ML part
As I mentioned in the first part of the presentation, channel estimation has been the conventional approach in wireless networks. However, with the advent of mmWave signals in 5G networks, beam selection has become another esteemed option for 5G networks
In 5G, we cannot use conventional channel estimation techniques anymore. We need sparse channel estimation techniques rather than conventional non-sparse channel estimation techniques
I believe another reason why a trivial beam selection is accepted in 5G standards is that there is still more research needed on the sparse channel estimation techniques
Perhaps we will see a sparse channel estimation approach applied in the next release of 5G standards
In our work, we use an existing algorithm in the literature called EM …
However, this part will be discussed at a later presentation because as you see here, there are 4 different topics that need to be covered. EM, AMP, VAMP, and Bayesian inference
The next presentation might be ready in January or February. Again, I will upload the video and slides on the same link seen on the first page of the presentation
You can say that these are statistical approaches which are known as CS techniques
In this presentation, I will talk why we need to do sparse channel estimation and why we can use compressed sensing techniques to achieve this. Then I will talk about the deterministic approaches such as ℓ_𝑝 minimization for sparse channel estimation. Finally, I will end the talk with a short connection between deterministic and statistical approaches
In our work, we use existing libraries written in Matlab for the estimation part and TensorFlow for the ML part. In general, we follow the footsteps of Prof. Schniter, who has publications and open-access libraries on these topics
The sparse Bayesian learning approach proposed by the …
The team who won the 3rd place also used SBL. They uploaded a short description of their proposal here.
The results of 2nd and 3rd places came close. However, Özlem, she utilized some other features of mmWave channels as well, so she could have that winning marginal difference.
In fact, the methodology I use is also similar as you see here, it reads Bayesian inference
A reason I choose VAMP is that the messages are passed in vector forms. So at every step, you do vector updates instead of scalar updates and I like to work with matrices and vectors.
Another reason is that VAMP is proposed by Prof. Schniter. I visited his lab for 6 months on a Turkish scholarship when I quit my full-time job to initiate my PhD thesis research right after completing my PhD courses.
To attend the lectures at the university, I compensated the missing work hours by working over-time at a Turkish telecom company, which has been in top-3 mobile service providers in Turkey
I am interested in Prof. Wen’s works as well. I met him in Taiwan. Thanks to this competition, I noticed Prof. Wen has also been doing research on these topics.
Prof. Wen replied my Asst. Prof. application positive when I was in Taiwan. However, I really liked the scope of the WASP project here and the Profs I will be working with. So I chose this position instead
As a future work, we might work on magazine or tutorial publication on statistical approaches for sparse channel estimation. In these publications, you are expected to give insights and intuitions of the algorithms without equations. Figures are allowed of course.
If we can have 1 or 2 more collaborators, it can be a timely publication

## Slide 27: CHANNEL TRAINING
, where (data transmission)
Beam training, (no CSIT)
  Design
  Select the columns of from
Channel training/estimation, (imperfect CSIT)
  Send pilot signals pilot signal (: pilot beamforming matrix, pilot symbols)
  instead of data signals (: data beamforming matrix, data symbols)
  Estimate the channel at the receiver by using the received pilot signal () and transmitted pilot signal ()
  (received pilot signal), : unknown
  (estimated channel)
  Design
Notes: Let me recap the first part of the talk from the last time briefly
y is the received signal vector …
U needs to be designed during the training phase
We can design U based on something else other than the channel
Or we can design U based on the channel
For the latter option, we need to do the channel training first
That is, send the pilot signals to estimate the channel first
Then design U based on the channel estimate
To estimate the channel, we send pilot signals, which is denoted by p. The pilot signal is known at both Tx and Rx sides
So when you receive the pilot signal, you have knowledge of both yp and p, then you can estimate H based on yp and p
Finally, you can design U based on this channel estimate

## Slide 28: CHANNEL TRAINING
Assume downlink (DL) data transmission, acquisition of channel state information at the transmitter (CSIT) options are
  Time division duplexing (TDD)
  Frequency division duplexing (TDD)
time
time
frequency
frequency
Notes: Training can be done via TDD or FDD
So let’s assume we want to do DL data transmission …
In TDD option, the BS and the mobile unit work at the same frequency f, but they transmit at different time slots
First, MU sends training/pilot signals to the BS
BS estimates the channel, designs its U matrix and then sends its data
In FDD option, BS and MU transmit at the same time but at different frequencies
BS transmits pilot signals, MU estimates the channel and sends feedback
Usually quantized feedbacks are sent, the exact complex channel values are not sent
Then BS can design its U beamforming matrix
BS and MU transmit nearly at the same time because MU needs some time to do the channel estimation
In FDD option, f is called DL frequency and f^’ is called the UL frequency

## Slide 29: ACQUISITION OF CHANNEL STATE INFORMATION
There are many approaches:
© [Qi2020]
CS: Compressed sensing
CS-based
sparse channel
estimation
Notes: As I mentioned before, we have two options in mmWave communications. We either do beam training or channel training/estimation
Here, in the first option of channel estimation approaches, you see CS based …
As I said, we need sparse channel estimation in mmWave networks and we can achieve sparse channel estimation by applying CS techniques
The second option is the conventional channel estimation techniques, and the last option is ML/AI based techniques
So, in this talk, we are interested in the first option

## Slide 30: COMPRESSED SENSING BASED
There are many approaches:
© [Qaisar2013]
Notes: In this figure, CS algorithms are unfolded in detail
In this talk, I will go through some of the algorithms categorized under these 3 branches
I will talk about three algorithms categorized under the convex relaxation branch, one algorithm categorized under the greedy iterative algorithms branch, and two algorithms categorized under the iterative thresholding algorithms branch. These are namely …
I will first talk about the convex relaxation approaches
Then the simplest iterative thresholding algorithms, IST, IHT and approximate message passing algorithm which is not shown here
Finally, I will end the talk by showing that in fact all these algorithms have a probabilistic view of point
This final point will be a short glimpse at Bayesian inference framework which we will cover next time hopefully
Let me briefly mention that in our work, we use the combination of these two branches
Particularly, SBL and belief propagation algorithms

## Slide 31: SPARSE CHANNEL ESTIMATION
In mmWave frequencies, the channel H is sparser, i.e., the number of non-zero elements is much smaller than the number of zero elements in H
Hence, the channel estimation problem can be cast as a sparse signal recovery problem
Sparsity does not manifest in the antenna domain but manifests in the angle domain
© [Mo2018]
(Wireless communications)
(Compressed sensing)
(see page 9)
Notes: So, what do we mean by sparse channels
In mmWave frequencies …
Hence, the channel estimation …
Here I used the term sparse signal instead of the sparse channel
In wireless networks, this is our equation where H is the channel matrix we want to estimate
Whereas in CS literature (I will explain the connection between the sparse channel estimation and CS techniques later), this is our equation where x is the sparse signal vector we want to estimate. Therefore, we need to transform our equation in the CS format
Also, you can call a vector as a signal, in general, in wireless communications. If you have a matrix, that means you have multiple signals as columns
If you remember, we had a channel matrix H that contained the random complex numbers between the antennas of transmitter and receiver
That H matrix in the spatial/antenna domain is not sparse
However, if we move to the angle or frequency domain, we see that the channel matrix is sparse in these domains
How do we move to a new domain?
It is almost as simple as the wavelength notion I mentioned in my last talk
The wavelength of a signal is equal to lambda=c/f, c is the speed of light. The unit of wavelength is in meters
If you do not have c there, then you have a period of a signal. Capital T is equal to 1/fundamental frequency. The unit of period is in seconds.
So by just including the parameter c, speed of light, we moved from the time domain to the spatial/space domain
You can do a transformation with a similar principle to move from spatial domain to angular or frequency domain
In short, for mmWave signals, sparsity manifests in angle or frequency domain but not in the antenna domain
Let’s see the angular domain first
Here you see the magnitudes of the channel matrix elements. Hij denotes the random complex number between the antenna indexes i and j at Tx and Rx, respectively
Therefore, this figure is in the antenna/spatial/space domain.
These axes are the antenna indexes at Tx and Rx
So this value here for instance is the magnitude of the channel between Tx antenna 20 and receive antenna 60
Apparently, H is a 60x60 matrix. That is, there are 60 antennas at both Tx and Rx
So, the channel in the antenna domain is not sparse
However, when you move to the angle domain, we can observe the sparsity
The channel matrix in the angular domain is denoted by H^S
As an example, assume there are 60 angular bins at both Tx and Rx
That is, at the Tx side, you divide the angular axis into 60 bins, at the Rx side same. You divide the angular axis into 60 bins so you have a 60x60 angular grid between Tx and Rx
Say you cover 180 degrees in total by your Tx antenna, so each bin (it is mostly called grid in mmWave literature) covers 3 degrees. Of course, you live in a 3D world so you have azimuth, zenith, and elevation (altitude) coordinates
As you see here, in the angular domain, the values are only gathered around two areas
Such as around grid indexes 40 at both Tx and Rx
And about grid index 50 at Tx and 10 at Rx
Clearly, H^S (S stands for sparse) is the sparse domain representation of H. Again, H^S is the angular domain form of H which in antenna domain

## Slide 32: SPARSE CHANNEL ESTIMATION
Line-of-sight and none-line-of-sight (due to scatters) propagations
mmWave (solid-colored lines): sparse in angular domain
mmWave + microwave (dashed-black lines): sparse in delay domain
© Scattering channel model and channel estimation in
fast time-varying and high mobility environments
by Chen and Fang
Amplitude
Time
: delay spread
Notes: The reason for the sparsity in the angular domain is that, at mmWave frequencies, the signals do not scatter much
Scattering means, your signal can multiply while traveling in the air, for instance by bouncing off the walls, desks, etc.
As a result, the same signal arrives in multiple copies at the receiver via LOS and NLOS paths
Therefore, you receive multiple copies of your signal from different angles
This figure can be considered to be microwave communications because the signal arrives at the destination via multiple paths due to the rich scattering
Scattering is a good thing actually because we can benefit from multiple copies of the same signal by using multiple antennas
But as I said in the first talk, we need to migrate to the higher frequencies, then we need to have more directional signals in mmWave frequencies
So, here you see that the signal arrives perhaps via only 3 paths at mmWave frequencies
This means the signal does not arrive at the user through many angles
This is one of the reasons why even the movement of your head while talking on the phone is a problem
In this figure, you see that the arrival times of the signals through the 3 paths are different
Their arrival times are different because they all travel at speed of light but the distances they travel are different
The difference between and is called the delay spread of the channel
At the receiver, you listen to the channel about the delay spread time
Clearly, mmWave signals are sparse in the delay domain because during the delay spread time (your observation duration), you receive only a few signals
In fact, the microwave signals are also sparse in the delay domain because the delay spread of microwave signals is larger
Perhaps you receive more signals during the delay spread but your delay spread is also long. So, microwave signals are also sparse in the delay domain
The reason for the sparsity in angular domain is that, at mmWave frequencies, the signals do not scatter much
Scattering means, your signal can multiply while traveling in the air, for instance by bouncing off the walls, desks etc.
Here as you see, you have LOS and NLOS paths
So you can receive multiples of your signal from different angles
Scattering is a good thing actually because we can benefit from multiple copies of the same signal by using multiple antennas
But as I said in the first talk, we need to migrate to the higher frequencies, then we need to have more directional signals. So, here you see perhaps the original transmitted signal and its only one copy due to the scattering on its way. We wished there were more copies on other angles
So the signal does not arrive to the user at different angles
This is one of the reasons why even the movement of your head while talking on the phone is a problem. Because if you move from your original spot, there are perhaps 1 or 2 more signals coming at you at different angles, so hopefully they will get to you at least
However, in delay domain, both mmWave and microwave signals are sparse. As I said, your signal multiplies in the air by bouncing off. Since each of them travels by light, and the paths they travel are different, these multiple copies arrive at different time instances
The difference between 𝜏_1 and 𝜏_max is called the delay spread of the channel. So at the receiver, you listen to the channel about delay spread time and during this time, you catch only few signals. While this is true for both mmWave and microwave communications, the delay spread of mmWave signals are shorter since as I said, they are more directional. So mmWave signals are even sparser in the delay domain

## Slide 33: SPARSE CHANNEL ESTIMATION
© [Mo2018]
Sparsity manifests in the frequency domain as well
© [Marques2019]
8 sinusoids in time and frequency domains
Tutorial
Notes: Sparsity can manifest in the frequency domain as well. Perhaps you are more familiar with this concept
As you know, Fourier transform of a sinusoidal signal gives you two Dirac delta functions, one at + and one at - frequency
If you have 8 sinusoidal signals with 200 samples for each, when you take the Fourier transform) of them, you have only 8 non-zero positive values in the frequency domain, and the rest of the samples are zero
So as you see here and in the previous slides, in general, by moving from one domain to another domain, we can find a sparse representation of a signal

## Slide 34: COMPRESSED SENSING
(Wireless communications, : unknown)
(Compressed sensing , : unknown)
: Measurement/Observation vector ( )
: Measurement/Sensing matrix
: S-sparse signal vector to be recovered
Compressed sensing
Assume
  𝑀≪𝑁: underdetermined system, ill-posed
Assume
  Underdetermined system Overdetermined system
measurements
non-zero values
: pseudo-norm
The number of non-zero elements
Notes: Let’s see what CS has to do with sparse signal estimation
We said, in CS literature, our equation is usually written as y=… whereas in wireless communications it is written as y=… So we need to transform our equation into this form. That is, x here must be a function of the H matrix
Let’s assume we have made that transformation and let’s use this equation
In CS jargon, y is, … A is …, x is …
S-sparse means the vector to be recovered has only S non-zero values which is much smaller than the vector’s dimension
As you know, this is l0 pseudo-norm operator which basically counts the number of non-zero elements in a vector
It is called CS because the number of measurements, M, is assumed to be much smaller than N
We said S is much smaller than N also, so this is the final equality between these parameters
While S is smaller than M, both are much smaller than N
That is, you want to recover your signal whose dimension is N in a much smaller dimension M. This is kind of a compression
You have an N-dimensional vector. You want to measure/sense this vector only M times which is a much smaller number than N, the dimension of your vector to be recovered, and still recover the x signal
Therefore, it is called compressed sensing
Is this possible?
The short answer is yes, it is possible due to sparsity of the x vector
Let’s first assume our x vector is not sparse and let’s assume it has N variables
Here is a visual look at our equation
If 𝑀≪𝑁, then we have an undetermined system. There are infinitely many solutions. Thus, this is an ill-posed problem
However, if the unknown vector is sparse, then the corresponding columns of A have no effects on the y vector
Therefore, by choosing the right columns of A, underdetermined system can be converted into an overdetermined system
Now let’s look at CS in more detail
CS has 3 main steps: Sparse representation, CS measurement (I call it compressed measurement in short), and reconstruction (recovery)
I just talked about the sparse representation in the previous slide in general
First, you need to find a sparse representation of h. For instance, you need to move to a domain where you have a sparse representation of h
So h is unknown and non-sparse, … x is unknown and sparse because the number of its non-zero elements is S which is a smaller number than its dimension
As you know, this is l0 pseudo-norm operator which basically counts the number of non-zero elements in a vector
Next stage is compressed measurements. That is, you have few number of measurements to do the estimation (reconstruction, recovery). The number of your measurements is compressed. That is M is much smaller than N
We said S is also very small and here is the relation between all three. S is smaller than M and both are much smaller than N
The last step is finally reconstructing/estimating h.
Basically, first you estimate x, but since you know the transformation, you can obtain h^as well
In CS literature, CS equation is given as y=Ax+n
Instead of sparse representation, that is, you find a basis matrix for sparse representation, you can directly do sparse approximation instead. If you have a signal vector with values [2.5 3 0.1 0.3 6] for instance, you can approximate those small values 0.1 and 0.3 to zeros. So you approximate the original signal vector [2.5 3 0.1 0.3 6] by a sparse signal [2.5 3 0 0 6]
y is the measurement vector…
The maximum number of non-zero elements in our sparse x is S
Another assumption is that this is an underdetermined system. That is, M is much smaller than N
Or in other words, the number of observations is much smaller than the length of the signal x to be recovered
Here is the visual representation
It is called CS because a high dimensional signal
Let’s look at the first step, sparse representation
In a sparse representation, the signal is represented as a projection on a suitable basis, i.e., a linear combination of only S basis vectors, with S ≪ N
In other words, the original signal h (N×1 column vector) can be represented with a basis of N×1 vectors {𝜳_i}_{i=1}^N
In the second step, the signal h is measured by the 𝛟 matrix. This might be easier to understand 2 slides later may be
I will talk about CS recovery (CS reconstruction), 3 slides later
In the next slide, let’s compare this CS equation with our main equation in wireless networks

## Slide 35: COMPRESSED SENSING
Assume
  Underdetermined system Overdetermined system
If the support of 𝐱 is known, i.e., non-zero locations, underdetermined system can be converted into an overdetermined system
measurements
Undetermined system
Overdetermined system
Notes: Again if x is a sparse vector and the support of …
Now let’s look at CS in more detail
CS has 3 main steps: Sparse representation, CS measurement (I call it compressed measurement in short), and reconstruction (recovery)
I just talked about the sparse representation in the previous slide in general
First, you need to find a sparse representation of h. For instance, you need to move to a domain where you have a sparse representation of h
So h is unknown and non-sparse, … x is unknown and sparse because the number of its non-zero elements is S which is a smaller number than its dimension
As you know, this is l0 pseudo-norm operator which basically counts the number of non-zero elements in a vector
Next stage is compressed measurements. That is, you have few number of measurements to do the estimation (reconstruction, recovery). The number of your measurements is compressed. That is M is much smaller than N
We said S is also very small and here is the relation between all three. S is smaller than M and both are much smaller than N
The last step is finally reconstructing/estimating h.
Basically, first you estimate x, but since you know the transformation, you can obtain h^as well
In CS literature, CS equation is given as y=Ax+n
Instead of sparse representation, that is, you find a basis matrix for sparse representation, you can directly do sparse approximation instead. If you have a signal vector with values [2.5 3 0.1 0.3 6] for instance, you can approximate those small values 0.1 and 0.3 to zeros. So you approximate the original signal vector [2.5 3 0.1 0.3 6] by a sparse signal [2.5 3 0 0 6]
y is the measurement vector…
The maximum number of non-zero elements in our sparse x is S
Another assumption is that this is an underdetermined system. That is, M is much smaller than N
Or in other words, the number of observations is much smaller than the length of the signal x to be recovered
Here is the visual representation
It is called CS because a high dimensional signal
Let’s look at the first step, sparse representation
In a sparse representation, the signal is represented as a projection on a suitable basis, i.e., a linear combination of only S basis vectors, with S ≪ N
In other words, the original signal h (N×1 column vector) can be represented with a basis of N×1 vectors {𝜳_i}_{i=1}^N
In the second step, the signal h is measured by the 𝛟 matrix. This might be easier to understand 2 slides later may be
I will talk about CS recovery (CS reconstruction), 3 slides later
In the next slide, let’s compare this CS equation with our main equation in wireless networks

## Slide 36: COMPRESSED SENSING
Overdetermined system
  e.g., Gaussian elimination if , i.e., full rank
  Least square if not full rank
Underdetermined system
  : norm,
    Cannot guarantee full recovery
  Sparsity helps
Notes: When we have an overdetermined system, we can, for instance, apply … when A is full rank
Or LS solution when it is not full rank
When we have an undetermined system, we can minimize l2 norm under this constraint
In fact, we will not use l2 norm but l1 norm. We will see the reason later
In this case, full recovery is not guaranteed indeed
In the last 3 slides, I wanted to explain, what CS algorithms have to do with sparse signal recovery, and how sparsity can help to recover a signal although we do compressed sensing
The example I showed that converts an undetermined system to an overdetermined system by choosing the columns of the sensing matrix A is known as matching pursuit algorithm which is a greedy iterative algorithm that I will detail later
𝑀≪𝑁 means, we have an undetermined system. Therefore, there are infinitely many solutions. Then this is an ill-posed problem
However, our unknown vector is sparse. Therefore, these corresponding columns of A have no effects on y vector
If we know the support of x, i.e., …, by choosing the right columns of A, underdetermined system can be converted into an overdetermined system
In y vector, there are no zeros although the colors are still grey
Here, in the A matrix, greys do not mean they are zeros, they just mean they do not have any effects
All in all, the basic idea of OMP is that find the non-zero locations of the x matrix. Create a new sub-system which is overdetermined. Solve for x.
You achieve this step by step. That is, column by column (of A) or element by element (of x)

## Slide 37: COMPRESSED SENSING
CS steps:
1st step: Sparse representation
, : basis matrix
2nd step: Measurement
: measurement matrix
3rd step: Recovery
Sparse approximation
© [Marques2019]
: Unknown, non-sparse
,
: Unknown, sparse
,
: Measurement vector
Notes: Now let’s look at CS in more detail
CS has 3 main steps: Sparse representation, CS measurement/observation/acquisition, and reconstruction/recovery
First, you need to find a sparse representation of h in a new domain
So h is unknown and non-sparse, … x is unknown and sparse
Next stage is the measurement/observation stage.
You have a few numbers of measurements. That is, M is much smaller than N
The last stage is reconstruction/estimation/recovery of h
In the sparse representation stage, the signal is represented as a projection on a suitable basis, i.e., a linear combination of only S basis vectors, with S ≪ N
In other words, the original signal h (N×1 vector) can be represented with a basis of N×1 psi vectors {_i}_{i=1}^N
In the second stage, the signal h is measured by the phi matrix
In the last stage, first you estimate x
Then, since you know the psi transformation, you can obtain h estimate from x estimate
Instead of sparse representation, that is, you find a basis matrix for sparse representation, you can directly do sparse approximation instead
If you have a signal vector with values [2.5 3 0.1 0.3 6] for instance, you can roll those small values 0.1 and 0.3 to zeros
So you approximate the original signal vector [2.5 3 0.1 0.3 6] by a sparse signal [2.5 3 0 0 6]
In other words, you are interested in the most important values
Now let’s look at CS in more detail
CS has 3 main steps: Sparse representation, CS measurement (I call it compressed measurement in short), and reconstruction (recovery)
I just talked about the sparse representation in the previous slide in general
First, you need to find a sparse representation of h. For instance, you need to move to a domain where you have a sparse representation of h
So h is unknown and non-sparse, … x is unknown and sparse because the number of its non-zero elements is S which is a smaller number than its dimension
As you know, this is l0 pseudo-norm operator which basically counts the number of non-zero elements in a vector
Next stage is compressed measurements. That is, you have few number of measurements to do the estimation (reconstruction, recovery). The number of your measurements is compressed. That is M is much smaller than N
We said S is also very small and here is the relation between all three. S is smaller than M and both are much smaller than N
The last step is finally reconstructing/estimating h.
Basically, first you estimate x, but since you know the transformation, you can obtain h^as well
In CS literature, CS equation is given as y=Ax+n
Instead of sparse representation, that is, you find a basis matrix for sparse representation, you can directly do sparse approximation instead. If you have a signal vector with values [2.5 3 0.1 0.3 6] for instance, you can approximate those small values 0.1 and 0.3 to zeros. So you approximate the original signal vector [2.5 3 0.1 0.3 6] by a sparse signal [2.5 3 0 0 6]
y is the measurement vector…
The maximum number of non-zero elements in our sparse x is S
Another assumption is that this is an underdetermined system. That is, M is much smaller than N
Or in other words, the number of observations is much smaller than the length of the signal x to be recovered
Here is the visual representation
It is called CS because a high dimensional signal
Let’s look at the first step, sparse representation
In a sparse representation, the signal is represented as a projection on a suitable basis, i.e., a linear combination of only S basis vectors, with S ≪ N
In other words, the original signal h (N×1 column vector) can be represented with a basis of N×1 vectors {𝜳_i}_{i=1}^N
In the second step, the signal h is measured by the 𝛟 matrix. This might be easier to understand 2 slides later may be
I will talk about CS recovery (CS reconstruction), 3 slides later
In the next slide, let’s compare this CS equation with our main equation in wireless networks

## Slide 38: COMPRESSED SENSING
CS steps:
Notation confusion between wireless communications and CS literature
© [Marques2019]
Received data signal | Received training signal H: unknown
: | SAME
: Data beamforming matrix | 
: Transmitted data symbols | : Transmitted pilot symbols
Received data signal | Received training signal H: unknown
 | SAME
Notes: I want to quickly go over the notation confusion in two different fields, wireless communications and CS literature
Remember that our equation of interest in wireless networks is y=Hx+n
Since we want to estimate the channel matrix H, we use pilot signals

## Slide 39: COMPRESSED SENSING
Received training signal H: unknown | Restructured received training signal x: unknown
 | ,
 | Measurement vector
: | : Measurement (sensing) matrix
 | : S-sparse signal vector to be recovered
: Transmitted pilot symbols | 
Received training signal H: unknown | Restructured received training signal x: unknown
Consider massive MIMO, i.e., is very large, and . Assume training time slots
, where , ,
To apply least square or least minimum mean square error (LMMSE)
Waste of resources, i.e., less time for data transmission: ,
where : coherence time, data transmission time
Number of receive/transmit antennas
Notes: Therefore, we must transform y=Hp+n into y=Ax+n where the new x is a function of the channel that we want to recover by CS techniques, and the A matrix is a function of p
We must restructure the equation to this version because we want to use CS based sparse recovery algorithms
In fact, by making the training time longer, we can have an overdetermined system
Consider ..
We can write the received training signal as follows
Hence, by making T large enough, we can apply …
However, this is waste of resources because if we do more training, then we are left with less time for data transmission
Here, you see the equation that reads coherence time is equal to …
Coherence time: the time duration where the channel matrix H does not change
During the coherence time, you need to do the training and then send the data

## Slide 40: CHANNEL TRAINING
Training,
…
In mmWave channels
: Number of RF chains at the receiver
: Grid sizes at the transmitter and receiver [Anjinappa2020]
E.g.,
e.g., see equations (8-13)
in [Fernandez2018]
=
: Measurement matrix
: Sparse representation matrix
Notes: We can see in mmWave papers that our main equation can be restructured in CS based recovery format
For example, you can check the equations from 8 to 13 in this paper
Again, let’s assume that the training phase is T time slots
Then you have T observed signals and thus, T measurement matrices
We have the same psi transformation matrix for all T time slots
If you remember, psi is the basis matrix for the sparse representation. We do sparse representation only once
So, here the assumption is that TM N so we need to apply compressed sensing
In mmWave, this inequality is like this……, where L_r
You can check this reference again for further info
I mentioned earlier about the grids/bins in the angular domain where the channel had a sparse representation
More formally, grid is about the discretization of the angular domain
This approach yields a finite set of discrete angle points, which are an approximation to the continuous angular space for mmWave signals
You can read more about grids in this paper
The typical values of these parameters for mmWave signals are …
As clearly seen here, mmWave channels need CS solutions
We can see in mmWave papers that our main equation can be restructured in CS based recovery format
For example, you can check the equations from 8 to 13 in this paper
As I mentioned in the first part of the talk, we must do training as the channel changes
Here, we assume that the training phase is T time slots
Then you have T observed signals and T measurement matrices
We have the same psi matrix for all T time slots of course. If you remember, psi is the basis matrix for the sparse representation
So, here the assumption is that TM ≪ N so we can apply compressed sensing
For mmWave channels, you can check the equations (8-13) again. In mmWave channels, the inequality can be …≪…, where L_r
Grid is about discretization of angular domain. This approach yields a finite set of discrete angle points, which are an approximation to the continuous angular space. You can read more about grids in this paper
Typical values of these parameters are …
If you remember, antenna numbers are also about 64, 128
I did not talk about hybrid antenna structures in the first part of the talk, but L, the number of RF chains at the transmitter or receiver, is the reason we have hybrid antenna structures. If we have full digital antennas, we need an RF chain for each antenna. So, by using analog precoders, we can have limited access but access to all antennas with less number of RF chains, and by using digital precoders with whatever number of RF chains available, we still have some gain from the digital part.

## Slide 41: COMPRESSED SENSING RECOVERY
: Measurement vector
: Measurement (Sensing) matrix
: S-sparse signal vector to be recovered,
, underdetermined system
Intuitive solution (assume no noise)
  : norm,
  : pseudo-norm, , i.e., count the number of non-zero elements
Convex relaxation:
  : norm,
How well is the solution? 
Does it provide sparsity? 
Notes: Now, let’s see the last step, the recovery step
From now on, I will simply use y=… equation
If we want to recover a sparse vector, the intuitive approach, assuming there is no noise for now, is to obtain the sparsest x vector; that is, the x vector with minimal number of non-zero elements, such that it satisfies the y=Ax equality
This is also called l0 minimization
If you remember p-norm, or l-p norm, of a vector is given by the sum of absolute to the power p values of the vector elements, and then take the 1/p power of the sum
l0 is a pseudo-norm since it does not satisfy norm properties such as constant scaling.
l0 pseudo-norm essentially counts …
l0 minimization requires an exhaustive search over N choose S combinations, which is impractical – NP complete
So, we can do convex relaxation by using l1 minimization instead. This optimization problem is known as basis pursuit algorithm.
We can use any linear programming algorithm for the solution of this problem
Now, two questions arise.
How well does this l1 norm solution solve compared to l0 norm solution?
Does l1 norm solution promote/provide sparsity?
The short answers to these questions are as follows
Under some conditions, l1 norm solution can recover the exact l0 norm solution
l1 norm solution provides sparsity
How about l2 norm solution? l2 norm solution does not provide sparsity

## Slide 42: COMPRESSED SENSING RECOVERY
How well is the solution?
Convex relaxation:
Restricted isometric property (RIP): needs to obey
Find the smallest so that any submatrix of is nearly isometric, i.e., norm of does not change significantly
Assume is Gaussian, then is sufficient, where is a constant
is a design problem either in a deterministic or in a random field
S
N
M
A
©
Notes: Now, let’s look at the first question in detail
How good can l1 minimization be compared to the l0 minimization which gives you the optimal result, but which is also NP-complete?
It is proved that if the sensing matrix A satisfies the RIP condition, l1 can exactly recover the l0 solution
For this condition to be satisfied, we need to find the smallest delta value …
This means the sensing matrix which compresses the domain from N to M should not alter the l2 norm of x much
Or we can also say that when we shrink the domain, the vectors in the new domain do not get close to or overlap on each other
This condition is also not easy to check because you need to do combinatory checks
However, it is proven that if you randomly design a sensing matrix whose size satisfies this condition, the probability of the matrix A satisfying the RIP condition closes to 1
There are two good news here
Your design consideration is only the size of the matrix
M is much smaller than N. M is approximately log of N. Assume we have N= 10^6, then log base 10 of 10^6 gives you only 6. M is only 6
This means you need approximately only 6 observations to do recovery

## Slide 43: COMPRESSED SENSING RECOVERY
Does it promote sparsity?
Assume
©
Tutorial/Lecture: 1, 2, 3, 4 (Matlab)
[Zhang2015]
Notes: Now, let’ look at the 2nd question. Does l1 norm promote sparsity?
To answer this question, let’s have a look at these famous drawings you see in many CS articles
Assume
Therefore, we have only one observation, that is we have only one equation, and two variables
We want a sparse solution. In this simple case, it means we want a sparse x^ vector solution which has only 1 non-zero element
These are the geometries of the solutions for different p values of the lp norm
These lines are the same and they correspond to the equality constraint
These are the cost contours. This is the contour for p larger than 1, between …
The solution exists when the line and the contour meet
As you know, when p=2, the contour is a circle. In this case, we are never likely to have a sparse solution
p=1 is a special case with good properties. Except the 4 cases, where the line can be on top of the edges of the contour exactly, the solution is always sparse
When p is between 1 and 0, we have this shape
As you see here, as p gets closer to 0, the solution can get sparser
Although there are papers for the cases when p is between 1 and 0, this approach is not the mainstream because lp norm between 0 and 1 is non-convex
Therefore, l1 norm is the most preferred relaxation
You can read more about the smoothness, global differentiability, and other properties of lp norms, and other discussions on the topic in the paper [Zhang2015]
You can check these links too. The last (4th) link has the Matlab codes to plot the contours/balls of the lp-norms in 2D/3D

## Slide 44: COMPRESSED SENSING RECOVERY
In the presence of noise
Unconstrained version
(Basis pursuit denoising-BPDN, or least absolute shrinkage and selection operator-LASSO) [Karseras2015]
Greedy iterative algorithms (OMP)
Iterative thresholding algorithms (IHTA, ISTA, AMP)
Speed/cost: (LP solutions) > Greedy > Thresholding
Notes: In the presence of noise, we can also relax the equality constraint by using l2 norm. Instead of making them exactly equal, we let be a margin of error between them
We can write this in unconstrained form (Lagrange form), which is known as BPDN or LASSO
As you know, BPDN and LASSO are similar. To have a closer look, you can check the thesis here
Eventually, we are interested in this unconstrained optimization problem
For real values, there is ½ in front of the first term, but for complex values, we can remove it
If I do not take a note on the following slides, it means I assume complex values
In the next part of this talk, I will talk about greedy … and iterative thresholding algorithms …
These are basic solutions
I will go through the other more advanced solutions in the next presentation
Although l1 is a good solution, for high dimensional problems, linear programming solutions and greedy solutions can be still too complex
So thresholding algorithms can be preferred for high dimensional problems

## Slide 45: ORTHOGONAL MATCHING PURSUIT (OMP)
Initialize (residual is initialized to the received/observed vector)
Step 1: Find the column index that is maximally correlated with the residual (modified observation)
where is the iteration number
Step 2: Update the submatrix , where is the column vector of chosen (via step 2) at iteration , i.e., stack the column selected at each iteration into the submatrix
Step 3: Estimate , where is the pseudo-inverse of
Step 4: Update , where
  (Repetitive selections of the same columns are avoided)
  By removing the contribution of from the observation vector , the identiﬁcation of the remaining nonzero elements is targeted in the next iteration
Step 5: Iterate until e.g.,
Notes: I will talk about only one of the greedy iterative algorithms, OMP
Again, the idea of MP algorithms, in general, is to find the non-zero locations in the x vector; that is, to find the support of the x vector
It equally means we need to pick the important columns of the sensing matrix A
OMP selects the columns of the sensing matrix A one-by-one
There are other variations, such as picking multiple columns at each step
Here, I try to explain OMP in 5 steps
First, you initialize your residual vector with the observed signal
It is called residual because the residual vector at step i is equal to the observed signal minus y_i^, where y_i^ is equal to the estimated signal at step i times the submatrix of the sensing matrix obtained at step i
This submatrix is composed of the selected columns of A. At step i, we select a column of A and then stack that column in the submatrix A_i
At the first step, we correlate each column of the A matrix with the residual vector and pick the column with the maximum correlation
If the correlation coefficient is high, that means, I found a non-zero location in x
We can interpret this step as follows
Assume that the normal of each column of A is nearly 1. If the x vectors has large numbers such as 100 and small numbers close to 0, then the correlation coefficient will be high for the column of A that corresponds to a large number in x.
I also put a simple experiment file here that illustrates this part only
After picking the column, we stack the selected column in a submatrix Ai
Now, you can do the least square solution because you are working with an overdetermined system since the submatrix Ai is composed of the selected columns
Next, you update the residual.
You can iterate this until your residual vector is very small or until you select S columns in case you know the sparsity of the x vector
It is called orthogonal MP because the residual vector vi is always orthogonal to the columns that have already been selected. Therefore, the same column cannot be selected again in the next iteration
In other words, the effect of the non-zero location of x just obtained is removed from the residual for the next iteration
As another option, of course, you can also keep track of the selected columns to avoid repetitive selection

## Slide 46: ITERATIVE THRESHOLDING ALGORITHMS
thresholding operator applied to each element of the input vector , where is the threshold parameter
Hard thresholding: , where is the element of vector , and is the indicator function
Soft thresholding: , where is the element of vector , and is equal to if and zero otherwise [Metzler2016, Zhang2015]
Shrinkage:
Notes: So far, we have seen convex relaxation and greedy strategies
We saw that LP algorithms or pursuit algorithms can be used
To repeat, greedy strategies like OMP are faster than LP solutions. However, greedy strategies can still be slow in large sized problems
Therefore, iterative thresholding algorithms can be preferred over the greedy algorithms
The simplest known thresholding algorithms are IHTA and ISTA
There are two steps in these algorithms
The first step is the gradient descent step, and the second step is the thresholding step
Let me first introduce the thresholding functions used in the second step
You can find two notations in the literature. The first notation is widely used whereas the second notation is mostly used in Schniter’s and his colleagues’ papers, or Schniter’s papers in short
r is the vector input to the thresholding operator and sigma is the threshold “parameter”
T can be S sometimes to denote the soft-thresholding
I believe this notation difference comes due to the Bayesian inference framework in Schniter’s works
When we talk about the probability distribution of x, we write p(x) as you know.
If want to specify that the pdf of x is dependent of a “parameter” sigma, we write p(x; sigma).
Or if we want to write the posterior probability of x, we write p(x|y; sigma)
I think he wanted to have harmony in the notations
For simplicity, here I assume real values, but these thresholding functions can be easily extended to the complex case
We can have a hard or soft thresholding
Hard thresholding function nulls the input if the input is a small value. Otherwise, it just passes the input
On the other hand, soft thresholding function shrinks the input by sigma towards zero if the absolute value of the input is larger than sigma, and nulls the input if the input value is small
Soft thresholding function is also called shrinkage function because it shrinks the input value by sigma
Here you see xn^ because as I said, thresholding algorithms are very simple. It is made of only two steps
After the gradient in the first step, we apply thresholding in the second step, where you obtain x^
The iterative thresholding schemes are naïve approaches since they rely on the assumption that the input to the thresholding function is the true signal plus a noise
So, by thresholding, we are trying to remove out the noise
Therefore, they are also called denoiser based algorithms and we can use more complex denoisers than the hard and soft thresholding functions
The term denoiser is used in a probabilistic setting/framework mostly; that is, when we assume the sensing matrix A is for instance Gaussian. I will get into that later

## Slide 47: ITERATIVE THRESHOLDING ALGORITHMS – ISTA
Convex + differentiable
Convex + non-differentiable
Apply proximal gradient descent
where
Lecture: 1, 2, 3
Notes: When we have convex sets, in fact, ISTA is the proximal gradient descent algorithm
Since g(x)…. h(x) is convex but non-differentiable, we can apply PGD by proximal mapping of the h function (l1 norm) because we cannot simply use the gradient descent algorithm
First, you apply the gradient descent for the g function and then apply the proximal operator for the h function
In explicit terms, you step away from your current estimate in the direction of negative gradient of your g function. Then you input this new value to the proximal mapping of your h function
The result of this proximal operation is well-known, and it is the simple soft-thresholding function denoted by S sub …
There is an important detail here. The threshold parameter is
For real numbers, this is but for complex numbers, it is only
So far, we have seen relaxation and greedy strategies. We said LP can be used for relaxation approach and pursuit algorithms can be used for the greedy approach
Greedy strategies like OMP are faster than LP solutions. However, they can still be slow
However, iterative algorithms can be faster than OMP
The simplest known is ISTA. For convex sets, ISTA is the proximal gradient descent algorithm
Since h(x) is convex + non-differentiable, we can apply PGD by proximal mapping of the h function (l1 norm) (we cannot simply use the gradient descent algorithm).
First you apply the gradient descent for the function and then apply the proximal operator
And the result is the proximal operator of l1 norm with the parameter 𝛽𝜆. For real numbers, it should be 1/2𝛽𝜆, but for complex numbers, it is just 1/𝛽𝜆
The result of this is a soft-thresholding of the input at the parameter 𝛽𝜆. This notation (S…) is more widely known and used. This notation 𝜼 is from Schniter’s papers. Also there might be a typo in his paper, the thresholding is given as 𝜆 but it should be 𝛽𝜆 I guess. So I just wrote sigma there as a general parameter

## Slide 48: ITERATIVE ALGORITHMS – ISTA
©
© [Maleki2011]
Iterative hard thresholding
Iterative soft thresholding
Notes: Now, I change the title to iterative algorithms for brevity
Also, from now on, I will use only Schniter’s notation
Again, first we do gradient descent on the least square term
Then we apply proximal operator on the l1 norm which is in fact a shrinkage/soft-thresholding function
It is visually shown here
On the right side, you see hard thresholding function, which takes you right on the axis at each step, whereas on the left, you slowly get close to the axis.
Because at each step, ISTA either shrinks or nulls the input whereas IHTA either keeps or nulls the input
So in these plots, the authors want to stress this difference

## Slide 49: ITERATIVE ALGORITHMS – ISTA
, where is the i.i.d. Gaussian noise and is the true signal
Assume no noise in the observation,
If is orthonormal, , then
Step 1: , where
If is orthonormal, , terminate
If not, , ,
Step 2:
If not, ,
Notes: In this slide, let’s move from deterministic setting to the random setting
We want to give an intuitive explanation roughly before moving on to the AMP algorithm because AMP is derived in the probabilistic setting
So we assume we have a random A matrix with Gaussian elements
In the random setting, it is easier to discuss that the shrinkage function acts as a denoising function
However, I will keep the discussion simple here
As I said before, by applying the shrinkage function to the input, we implicitly assume that our input to the shrinkage function is a noisy observation of the true x signal which is denoted by x0 here
Let’s assume the noiseless case
If A …, that is …, then A^Hy=… can recover us the true signal
At step 1, we apply A^Hy, which can be rewritten as …
If A is orthonormal, we can terminate because we can recover the true signal
If not, Bx0 cannot be equal to zero, then we have the true signal plus a noise term whose power is Bxo norm square
So if we can set the threshold to the standard deviation of noise, we can recover the true signal
But assume we have some x^ estimate from the first step by choosing some threshold. And we know from our experience that this estimate will be closer to x0
Then in the next step, we subtract the y^ estimate from y, that is we evaluate the residual y-Ax^, which can be rewritten in this format
Again if A is orthonormal…
If not, again we have a noise term but this time, the noise power is smaller than the noise power in the first iteration
Therefore, in the second step, we are expected to achieve a more accurate estimation since the noise power is lower than the noise power in the previous step
As a result, at each iteration, we are expected to get more accurate results
To repeat again, in this slide, we learn two things
Iterative thresholding schemes are naïve approaches since they assume the input to the shrinkage function is the true signal plus a noise
Then we understand that our eta function is in fact a denoising function
We can use more complex denoising functions for wireless communications applications that can be borrowed from image denoising publications
We will talk about these advanced denoisers soon

## Slide 50: ITERATIVE ALGORITHMS – AMP
Onsager correction term
Presentation/Tutorial: 1, 2
Iterative shrinkage/threshold algorithm (ISTA)
, where
Approximate message passing (AMP)
and
: tuning parameter
: Pseudo-data, shrinkage/threshold input
Notes: Now, let me introduce the AMP algorithm
To compare side by side, here I rewrite the ISTA steps by introducing the residual variable v
For the same LASSO problem, AMP solution is given here
As you see, the iterations are almost same with ISTA except two points
  You have the additional term which is called Onsager correction term
  Your threshold is iteration dependent. The threshold value changes with iteration and the threshold is set equal to the standard-deviation of the residual term
I want to talk about the AMP algorithm by words only at this point
These steps are derived through AMP technique in a probabilistic setting. For ISTA, we do not have such a probabilistic derivation
Message passing techniques, also known as belief propagation techniques, are for high dimensional problems
Therefore, under high dimensional problems, we can do approximations in the probabilistic setting such as by using the central limit theorem (Taylor series approximation is also used just to note)
AMP algorithm is proven to be accurate in the large system limit when M/N converges to a constant as M and N scale to infinity
As I said, I will get into these details in the next presentation
But for now, we can learn that these steps are derived from a probabilistic perspective by using the AMP technique

## Slide 51: ITERATIVE ALGORITHMS – AMP
Benefit of Onsager correction term
Does behave Gaussian?
Numerical evidence [Donoho2010]
Rigorous support [Donoho2011]
© [Metzler2016]
Notes: So what is the benefit of the Onsager correction term?
The benefit of the Onsager correction term was first observed numerically, later strong theoretical evidences were provided in a follow up publication
The question here is, does the input really behave like true signal plus a Gaussian noise?
If so, then the input minus the true signal should give us a Gaussian noise
Here, you see QQ plots of ISTA and AMP algorithms for the input minus true signal
Please remember that the residual vi has Onsager correction term in the AMP algorithm whereas in ISTA, we do not have the Onsager correction term
QQ plots show us how Gaussian the input distribution is
If the blue sample dots are straighter; that is, they lay mostly on the red line, this means the input distribution is closer to Gaussian
As see in the edges here, AMP algorithm provides a more Gaussian distribution than the ISTA algorithm due to the Onsager term
In this example, BM3D denoising function is used which is originally proposed for image denoising application but which can also be used for wireless communications applications

## Slide 52: APPROXIMATE MESSAGE PASSING (AMP)
AMP for any Lipschitz-continuous shrinkage function:
and
: derivative of , : average of a vector, : element of vector , and div is the divergence operator, : partial derivative
are different notations used in the literature
When is a large i.i.d. sub-Gaussian matrix, can be modelled as , where is the true signal
Initially, observed by numerical evidences that the Onsager correction assures the approximation
Later more rigorous evidences are provided
Notes: AMP can be used with any Lipschitz continuous shrinkage function
In this case, b is evaluated by the derivative of the shrinkage function and then taking the average of the elements
These are different notations used in the literature
eta^prime, partial differential, and divergence notations are all used in the literature
Here, I repeat the same comments I told earlier

## Slide 53: DENOISING BASED ALGORITHMS
Divergence evaluation via Monte Carlo
In theory:
, where
and is very small
In practice:
  Generate ,
  Evaluate ,
  where and is very small
  If is high dimensional, is sufficient
Linear model (AMP) Generalized linear model (GAMP)
Notes: Again, AMP is a denoising based algorithm
Like the BM3D denoising function mentioned earlier, different denoising functions can be used
For complicated denoising functions, the divergence evaluations might be challenging
In that case, we can do divergence evaluation via Monte Carlo simulations
We can generate multiple b vectors each with a normal distribution
Then we evaluate the divergence for each random generation with a very small epsilon value
And then average over all obtained divergence values
If r is a high-dimensional vector, only one-time generation is usually sufficient
Again, so far, we have only been discussing denoising based algorithms such as AMP-ISTA, AMP-BM3D, or other denoisers with AMP.
Because, again, all of them rely only the simple assumption that the input to the denoising function is the true signal plus a Gaussian noise
Because, in this presentation, we have only focused on the linear model which is y=Ax+n
AMP is later extended to a more general setting known as generalized linear model
In the GLM, the input has a distribution, it is called prior distribution
In GLM, there is also a likelihood probability distribution for the observed y vector
So this model is also called Bayesian GLM
The extension of AMP to Bayesian GLM is known as generalized AMP (GAMP)
Again, I will talk in more details about these in the next presentation

## Slide 54: BAYESIAN INFERENCE MODELS
Likelihood function:
Maximum likelihood estimate of
(Least squares solution)
Prior distribution: (Laplace distribution)
Posterior distribution:
Maximum a-posteriori estimate
(BDPN, LASSO)
Notes: In this and the next slides, I will briefly show that in fact the deterministic approaches we have seen have probabilistic correspondences
So you can assume this slide is an entry to Bayesian inference models where we work with probabilistic models
Again, assume a linear model with a Gaussian noise
Given x and noise power, the likelihood function is again a Gaussian with …
ML … can be written as argmin of –log of the likelihood
When we take the –log of the right-hand side, we obtain a constant plus the least square term. That is we have a LS problem
We can assume we have a prior information on x with parameter v. That is we know p(x|v)
Then from Baye’s theorem, posterior distribution of x can be written as the likelihood of y times prior distribution of x
Then we can do MAP estimation
When we take the –log of the right-hand side, we obtain the least square term plus the l1 norm which we know as BDPN or LASSO problem
As you see in this slide, deterministic approaches have probabilistic correspondences

## Slide 55: BAYESIAN INFERENCE MODELS
: Gaussian, Laplace, Student-t
© [Karseras2015]
© [Seeger2010]
Prior:
Posterior:
Gaussian
Student-t
Notes: In this slide, we can see that prior distributions have lp norm correspondences
Here you see the prior distributions of Gaussian…
If we use Gaussian distribution, that means we are using l2 norm. If we use Laplace …
Clearly, Gaussian and Laplace are log-concave functions but, student-t is not
As seen in their posterior distributions, Gaussian prior provides nothing but uniformly distributed variables whereas Laplace and Student-t provide variables skewed toward the axis
Although Student-t promotes more sparsity, we just said it is not log-concave so it is not preferred
Gaussian distribution is log-concave but it does not promote sparsity
So Laplace distribution which corresponds to l1 norm is a good choice for our purpose

## Slide 56: APPLICATION OF AMP TO BAYESIAN INFERENCE FRAMEWORK
Another approach for solving
is the Bayesian framework. In a Bayesian framework, prior density and likelihood function is assumed on , to evaluate the following posterior density
Then, the posterior density can be used to evaluate the MMSE estimate
where is the expectation operator
Instead of the notation for the denoising function, let us use the notation where is the precision of the noise
Notes: In this and the next slides, I just write down the theoretical formulas which cannot be used in real problems
In the next presentation, I would like to start from the basic theory
I plan to start with the notions mostly from Kay’s statistical signals books
Then I will step-by-step move towards the realistic settings
I will explain Bayesian inference/learning, expectation maximization, message passing algorithms and so on
Therefore, I would like to stop here
My suggestion is to go through all links and references provided in this presentation
This presentation is a blend of all these resources in fact
In these resources, you can understand more and clearer about the intuitions I tried to explain. You can find more connections in the theories at high levels
Of course, for the transaction and thesis resources I provided, you can find the full details
These resources will lead you to other valuable resources as well
During the presentation, sometimes, I shared resources just because of the copyright issues, because I borrowed their figures. I think you can identify them
In short, in this presentation, I tried to touch many points in a short time for the purpose that this presentation might be a steppingstone for you to move on to those references I provided
Thank you for listening

## Slide 57: APPLICATION OF AMP TO BAYESIAN INFERENCE FRAMEWORK
Assume i.i.d. prior
AMP can be applied to the MMSE problem of Bayesian framework by choosing the denoiser as
(Iteration index is dropped)
Derivative of the above scalar MMSE denoiser is given as
,
where is the variance operator, and
AMP can diverge when the measurement matrix is even mildly ill-conditioned or has nonzero mean
Vector approximate message passing (VAMP) is much more robust than AMP, i.e., when is even highly ill-conditioned or has nonzero mean
Explaining further intuitions behind VAMP and Bayesian inference require significantly more slides and time. Covering these topics in another presentation is more feasible

## Slide 58: NUMERICAL RESULTS
In progress
Currently, further improvement of the normalized mean squared error (NMSE) of the channel estimate is being focused

## Slide 59: REFERENCES
[Anjinappa2020] C. K. Anjinappa, A. C. Gurbuz, Y. Yapici, and I. Guvenc, “Off-Grid aware channel and covariance estimation in mmWave networks,” IEEE Trans. Commun., 2020.
[Choi2017] J. W. Choi, B. Shim, Y. Ding, B. Rao, and D. I. Kim, “Compressed sensing for wireless communications: Useful tips and tricks,” IEEE Commun. Surv. Tutorials, 2017.
[Donoho2010] Message passing algorithms for compressed sensing: I. Motivation and construction, IEEE Trans. Inf. Theory, 2010
[Donoho2011] The Dynamics of Message Passing on Dense Graphs, with Applications to Compressed Sensing, IEEE conf., 2011
[Fernandez2018] J. Rodríguez-Fernández, N. González-Prelcic, K. Venugopal, and R. W. Heath, Jr., “Frequency-Domain compressive channel estimation for frequency-selective hybrid millimeter wave MIMO systems,” in IEEE Trans. Wireless Commun., 2018.
[Karseras2015] E. Karseras, “Hierarchical Bayesian models for sparse signal recovery and sampling”, PhD thesis, 2015.
[Maleki2011] A. Maleki, “Approximate message passing algorithms for compressed sensing,” PhD thesis, 2011.
[Marques2019] E. C. Marques, N. Maciel, L. Naviner, H. Cai, and J. Yang, “A review of sparse recovery algorithms,” in IEEE Access, 2019.

## Slide 60: REFERENCES
[Metzler2016] C. A. Metzler, A. Maleki, and R. G. Baraniuk, “From denoising to compressed sensing,” in IEEE Trans. Inf. Theory, 2016.
[Mo2018] J. Mo, P. Schniter, and R. W. Heath, “Channel estimation in broadband millimeter wave MIMO systems with few-bit ADCs,” in IEEE Trans. Signal Process., 2018.
[Qaisar2013] S. Qaisar, R. M. Bilal, W. Iqbal, M. Naureen, and S. Lee, “Compressive sensing: From theory to applications, a survey,” in J. Commun. Networks, 2013.
[Qi2020] C. Qi, P. Dong, W. Ma, H. Zhang, Z. Zhang, and G. Y. Li, “Acquisition of channel state information for mmWave massive MIMO: Traditional and machine learning-based approaches,” June 2020. [Online]. Available: http://arxiv.org/abs/2006.08894.
[Rangan2019] S. Rangan, P. Schniter, and A. K. Fletcher, “Vector approximate message passing,” IEEE Trans. Inf. Theory, 2019.
[Seeger2010] M. W. Seeger and D. P. Wipf, “Variational Bayesian inference techniques,” in IEEE Signal Process. Mag., 2010.
[Zhang2015] Z. Zhang, Y. Xu, J. Yang, X. Li, and D. Zhang, “A survey of sparse representation: Algorithms and applications,” in IEEE Access, 2015.